## Slide 1
Morris Training
Creating a Product
Adding Products to Tank
Section 3

## Slide 2
Press on the Top area of the Tank- to open the Product Configuration Window Note: You must have the Tank fully expanded.

## Slide 3
Press on the Product Name Window

## Slide 4
Select New Product and Hit the Green Check Mark

## Slide 5
Chose Custom Product, proceed by pressing the Yellow Forward Arrow after each step

## Slide 6
Tap on the PRODUCT NAME

## Slide 7
Enter a product name, as an example we are using CAN-BLEND-2020, followed by the Green Check Mark

## Slide 8
Proceed with the Yellow forward arrow

## Slide 9
Enter the density of the Product. The density of the product can be requested From Your Seed Or Fertilizer Supplier. If a density is not available proceed with the default value.

## Slide 10
If you would like to enter the density, press on the Product Density Tab

## Slide 11
Enter the new density value from the product supplier. Followed by the Green Check Mark

## Slide 12
To continue press the Yellow Arrow

## Slide 13
Enter Product Rate increment and Preset Rates.
Rate increment- Used for quickly bumping the rates up or down (+/-) while moving.
Preset 1 – Enter the desired rate you will be seeding at.
Preset 2 – Can be used as a secondary rate as desired, example a lower rate used on hilltops or areas of the field which do not require as much product

## Slide 14
Proceed by touching the Green Check Mark

## Slide 15
Add a generic Calibration Factor
Press Manual Entry Icon

## Slide 16
Enter a generic value of 2.25lb/ac, followed by the Green Check Mark
Review the product data, once satisfied with the values Apply with the Green Check Mark

## Slide 17
You will be prompted to Fill the Tank with the new Product. You can choose to fill the tank at this time. If you are satisfied, Click Yes

## Slide 18
Adding Products to Tanks

## Slide 19
To access the Global home screen menu, Swipe up and press the
Home icon.
Select Seeder-Home

## Slide 20
Expand the Tank you wish to add the Product into by pressing on the Title Bar

## Slide 21
Press on the Top Area of the Tank – to open the Product Configuration Window

## Slide 22
Press the Product Name <Select Product> tab

## Slide 23
Select Product from the list. Proceed by pressing with Green check mark

## Slide 24
Review the Rate Presets and Rate Increment settings

## Slide 25
Press on the Calibration Factor window.
If this is the first time using a product adding a cal. factor will shorten calibration time.

## Slide 26
Press Manual Entry

## Slide 27
Press the Cal Factor Icon.

## Slide 28
Using the keypad enter the following Cal factor 2.25 lb/Rev
Review the Cal Factor is set, press the Green Check Mark

## Slide 29
Review the settings are correct press the Green Checkmark.

## Slide 30
Do you want to fill the Tank with the New Product? Yes

## Slide 31
Tank 1: has been filled with the desired product CAN-BLEND-2020.
Note: Preset 1 is automatically populated in the requested Rate window 60lb/ac.

## Slide 32
Press the Title Bar to Minimize Tank 1
Continue to fill all 4 tanks the same as you did Tank 1

## Slide 33
Manually Filling Tanks
With tank view expanded- Touch Tank Fill Window

## Slide 34
Press the Weight icon
Using the keypad enter the Weight manually. Proceed by pressing the Green Check Mark
Use this method If you know the how much the product you are using weighs

## Slide 35
If you do not know the product weight use this method.
Touch the single “Beer” glass to fill the tank you are on
Touch the 3 “Beer” glasses to fill all tanks to capacity
NOTE: Without knowing your actual weight this method only gives you an estimate on how much product is remaining in your tanks

## Slide 36
Select Green Check Mark to save